## Slide 1: Space charge dominated beam issues
G. Franchetti, GSI
Performance Computing at CNAF: Accelerators and Plasma Physics
Bologna, 24-6-2014

## Slide 2: Outline
Introduction
Physics case
Outlook

## Slide 3: The next generation of computational challenges at FAIR
New: Cooled pbar Beams (15 GeV)
Intense Cooled Radioactive Beams
Parallel Operation
Primary Beam Intensity | x 100-1000
Secondary Beam Intensity | x 10 000
Heavy Ion Beam Energy | x 30

## Slide 4: The SIS100 challenges
Storage time 5 x 105 turns
Intensity 1.5 x 1011/ions U+28
Space charge tuneshift Q ~ 0.2
SIS100 has SC dipoles --> Nonlinearities
Beam loss prediction
Localization of beam loss
Emittance increase prediction
Lattice design:
Collimation system
Magnet quality:
Nonlinear field control
Resonance
compensation system
Coherent instability threshold with space charge in the
FAIR rings.

## Slide 5: Space charge and resonances
Project motivation:
FAIR Project  SIS100, LIU @ CERN
Physics background:
The beam physics case is the overlapping of the tune-spread
with resonances, collective resonance are not of concern
over the long term (?)
Issue:
Beam behavoiur at injection plateau (~ 105 turns)

## Slide 6: The physics case
Operation with large incoherent tunespread in a nonlinear synchrotron
K. Schindl CAS

## Slide 7
Periodic crossing
of a resonance
z
x
Bare tune
Lattice error or
Space Charge Structure
Resonance
Slow halo
formation
If halo is too large
slow beam loss
take place
Pipe
z

## Slide 8: Motion of particles
G. Franchetti, I. Hofmann NIM A 561, (2006), 195-202

## Slide 9: The complexity of the self-consistency
detuning
Resonance condition
Particle amplitude
growth
Beam size
growth
Particle
loss
Halo particles

## Slide 10: The long term effect of PIC noise
J. Struckmeier Phys. Rev. E 54, 830−837

## Slide 11: Computing challenges: example
Integration steps/turn: 20 x Qx = 20 x 18 = 360
Grid resolution of the beam: +/- 10 grid points
Typical beam pipe/beam size ratio = 6
Transversally 125 x 125 grid points
Longitudinally keep the same 125 grid points
Statistical fluctuation of 1% -> 104 particle/grid cell
PIC parameters
N = 100 x 106
particles
Tracking a bunch for 5 x 105 turns means:
Compute the space charge of 100 x 106 particles
for 200 x 106 integration steps

## Slide 12: Space Charge effects
Coherent
Incoherent

## Slide 13: Long term simulation with frozen models example with SIS100
Typical pattern of beam loss for a frozen
beam tracking
Frozen model: means that the source of detuning with amplitude remains unaffected by the beam loss
normal sext
skew sext
normal quad
skew quad
skew sext
normal quad
One error seed
G. Franchetti, S. Sorge Proc. of IPAC2011, S. Sebastian, Spain. MOPS002

## Slide 14: Correcting 2nd, and 3rd order, normal and skew resonances
first bunch
G. Franchetti, S. Sorge Proc. of IPAC2011, S. Sebastian, Spain. MOPS002

## Slide 15: PS measurements 2002-2003
G. Franchetti, I. Hofmann,
M. Giovannozzi, M. Martini, E. Métral Phys. Rev. ST Accel. Beams 6, 124201 (2003).
E. Métral, G. Franchetti, M. Giovannozzi,
I. Hofmann, M. Martini, R. Steerenberg Nucl. Instr. and Meth. A 561, (2006), 257-265

## Slide 16: Bunched Beam, Higher intensity
measurement
simulation
ΔQx = −0.04/ − 0.045

## Slide 17: Bunch length – beam loss correlation
Experiment

## Slide 18: PS measurements 2012
R. Wasef, A. Huschauer, F. Schmidt, S. Gilardoni, G.Franchetti
qy0 = 6.47
1.1s
Resonance:
qx+2 qy = 19
I = 2A
Dqx = -0.046
Dqy = -0.068
Measurement
Qx0
SPACE CHARGE 2013

## Slide 19
initial
final
qy0 = 6.47
qx0 = 6.11
Y [mm]
qy0 = 6.47
qx0 = 6.11
vertical
horizontal
Simulation
Simulation

## Slide 20: Outlook
The effect of space charge on a synchrotron appears to be very sensitive
from the detailed knowledge of the machine.
The impact of resonances on space charge is dramatic, and
the effectiveness of the resonance compensation in presence of space
charge is not experimentally demonstrated yet.
The effect of self-consistency in case of thick halo may play a role,
Effort to change from frozen models to PIC models.
ISSUES:
PIC noise control
optimization parameters for speeding up simulations
benchmarking beam loss (very demanding)
Using code for beam physics studies / design issues
Synergy between accelerator physics and computer science is the most welcome!