## Slide 1: Storage an experiment overview
(with a StoRM perspective …)
Tommaso Boccali – INFN Pisa

## Slide 2: Caveats
For RunII (and possibly RunIII) the LHC Experiments’ computing models have been updated “recently”, so we have a guidance
No official document exists for RunIV (Today+10y), so we move into a crystal ball approach
Given the last point, experiments do not seem keen on stating (too) precisely the plans, since
  They really do not have a precise landscape
  They do not want to commit too early
What you find here for the long term scenario is from private communications, my take on the subject, etc… Don’t blame experiments!
This is even more true for non-LHC experiments, which usually have shorter horizon models; I will focus on LHC Experiments

## Slide 3: LHC Schedule & RunX definitions
RunII
RunIII
RunIV
RunV
RunVI

## Slide 4: LHC Luminosity profile
today
Expect by RunVI (pp):
15x Inst lumi wrt 2015
100x Int lumi wrt 2015

## Slide 5: Run#, terminology (pp, for ATLAS and CMS)
Run2: 2015-2018
  Up to 1.5e34, 25 ns, 13 TeV – up to 50 fb-1/y
    <PU> = 40
Run3: 2021-2023
  Up to 2.5e34, 25 ns, 13 TeV - up to 100 fb-1/y
    <PU> = 60
Run4: 2026-2029
  Up to ~5e34, 25 ns 13-14 TeV – up to 300 fb-1/y
    <PU> = 140 if not 200 (limit comes from leveling, not from LHC)
This is “Phase2” for pp
1 y
6 y
11 y

## Slide 6: LHC is not the only source of scaling factors
Resource needs scale also with what Experiments want to collect / process
ATLAS, CMS:
  All adiabatic till RunIII included. Resources requested scale with Inst Lumi and mildly with Int Lumi; Trigger rate stable ~ 1kHz
  RunIV:
    Up to 10 kHz Trigger, up to 7.5e33 cm-2s-1: this alone brings a factor ~100x
ALICE, LHCb:
  RunIII is the breaking point. Large Trigger rate increases
    ALICE up to 50 kHz, LHCb up to 50 kHz
  Increase in Lumi (decrease LHC leveling @ point 8): LHCb up to 2xe33 cm-2s-1

## Slide 7
Computing Resource scaling
CPU: scales
  Linearly with trigger rate (if you process everything you collect)
  More than linearly with <PU>, # tracks, …
  Scales with data integrated over some typical window (2-3 years)
  Analysis: scales also with # of concurrent analyses
Storage: scales
  Linearly with trigger rate
  Less than linearly with <PU>, …
  Scales with data integrated since the start (at least the tape)
If you plug in rates, event complexity, s, etc, you end up with
    Totals wrt Run1: Run2(3) = ~6-10, Run4 >100
Various Trigger Levels
OFFLINE
Rate
#sec/year
Event Size
<PU>

## Slide 8: Resource deployment - 2015
From Rebus/WLCG
T0: 700kHS06, 50 PB Disk, 100PB Tape
T1: 1MHS06, 100 PB Disk, 200 PB Tape
T2: 1.5MHS06, 100 PB Disk
… and scaling, mostly all approved by now

## Slide 9
Chart: 
| Run 1 | Run 2 | Run 3 | Run 4
LHCb | 1.3 | 2.7576 | 9.1919 | 9.1919
ALICE | 3.4725 | 4.63 | 92.6 | 92.6
ATLAS | 2.4 | 7.0707 | 7.0707 | 101.0101
CMS | 1.2 | 6.65 | 6.65 | 200
Very rough estimate of a new RAW data per year of running using a simple extrapolation of current data volume scaled by the output rates.
  To be added: derived data (ESD, AOD), simulation, user data (which is easily a big factor)
The different experiments have different timing:
ATLAS/CMS: Run4 is the inflation
LHCb/ALICE: Run3
PB
Buncic™
RAW DISK/TAPE

## Slide 10: Let’s move to storage needs/use patterns
The initial Computing Models had a clear distinction for protocols for
  WAN data movement (in the MONARC hierarchy):
    Human driven (later also algorithms)
    Throughput oriented protocols, with full fledged security model
    Tape aware, Space token aware
    SRM as protocol, many implementations
      CASTOR, DPM, BeStMan, dCache, StoRM…
  LAN oriented protocols, internal to sites
    Posix, RFIO, Xrootd, Dcap, ....
    More optimed (not all) for random access
    Not necessarily implementing a security model apart from the Posix one

## Slide 11: RunII Situation – Exec summary
Apart from ALICE (which stands differently from the others for the whole talk), SRM is still the main interface for WAN file transfers
Used for Disk <-> Disk, Disk <-> Tape
Indeed, already in 2011, WLCG TEG recommended (among other things) that SRM is an overkill for any transfer not involving tape
  Experiments seem indeed quite open in that direction

## Slide 12: SRM servers used as of today @ T1s
CERN: CASTOR + EOS
ASGC: CASTOR
BNL: dCache
CNAF: StoRM
FNAL: dCache + EOS
IN2P3: dCache
JINR: dCache
KISTI: DPM
KIT: dCache
NDGF: dCache
NL-T1: dCache + DPM
PIC: dCache
RAL: CASTOR
RRC-KI-T1: dCache
TRIUMF: dCache
T2s+T3s: mostly dCache and DPM, some with StoRM (30 as far as I was told…)

## Slide 13: New (more or less expected) perspectives for the future - Expected
Remote access protocols:
  XrootD
    Historically the main protocol for ALICE for … everything
    Initially planned by the rest of the LHC Experiments as fallback, i.e. in order to strengthen the infrastructure
    RunII: expected ramping of remote reads on purpose
      CMS: up to 20% of the access from jobs as remote; ATLAS: up to 20% of the WAN bandwidth
      Either user driven (BAD: send jobs uncorrelated with data location), or System Driven (Overflow by the WM, which takes into account limits, “network vicinity”, etc)
      In general, access structured in Federations, which try and insure the best network path (w/o a global location DB, in order to allow sites to pop in/out dynamically)
  WebDAV/Http
    Reaching same functionality levels, a bit behind as Experiment Support
        ATLAS better than CMS, currently;

## Slide 14: Less expected (at least as scale)
Due to budget problems (and, realistically, to the huge increase of requests), opportunistic computing / commercial procurements are becoming an essential part of the Exps’ computing models – See ATLAS
While it is “easy” to buy/find Computing resources, it is less true for Storage
This drives into some different directions
  (Dynamic) Data Caches
  (Again) remote access
  In case of local storage, be ready to accept whatever is offered
    S3 is an example
  These directions are barely touching a standard “owned” Tier Site
Other site-related dynamics:
  Example is RAL willing to go Ceph/S3 entirely, w/o SRM support at ALL

## Slide 15: On the same page ($$$)
All the experiments would LOVE limiting the tape usage (and thus the SRM interactions) to the bare minimum
  Permanent Storage of RAW data
  Temporary (but ~ long term) storage of reference samples
In the presence of sizeable Disk resources, the Tape would be ~ never read back
  A very few times, like for a global reprocessing at a end of a Run – not a year!
Reality is that in periods of budget problems tape storage (~5x cheaper than disk) is going to be used also as a fast turn-around low-quality disk area, which increases a lot
  Number of recalls per file
  Deletions, repacking, bandwidth needs, stress on readers
  (SRM utilization more on the critical path)

## Slide 16: More complex patterns?
In most of our sites (HDFS ones being the exception), a separation Storage / CPU is present
This has proven optimal from the Sites’ operational point of view, is that ok for the future?
Machine Learning and Big Data are the new buzzwords for efficient large scale data analysis, and they come with a price:
  Hardware and Software are more entangled in order to maximize performance
  Tools like Spark, Pig, Hive require a different hardware setup, and Experiments can request on the longer run to have specific centers – if the standard architectures are not able to fulfill

## Slide 17: Authorization / Authentication
Which is the future of these aspects?
X509 is ok for standard (GRID) use, but what if we start writing / reading via SRM from Clouds / Opportunistic / portals?
There preferred AAIs are SAML, ID-Federations, and such. We need a bridging, and indeed there are some efforts around this.
Does this have direct impact on SRM/StoRM?
  Are you relying on external bridging services?
  Are you planning to have these protocols internally supported?

## Slide 18: Feature explosion
For example:
  Right now StoRM supports also WebDAV
    To my understanding, preferred over WebDAV on GPFS/Posix just for ACLs
  On the other hand, Xrootd supports WebDAV
    I understand it better, since in this case Xrootd also serves as disk merging tool
General message I gathered from the experiments: in case of support issues of StoRM, better focus on the core functionalities (SRM)
If we can vote, new functionalities are much lower priorities than maintaining the tape functionalities, which are unique and essential to SRM

## Slide 19: This is all real, not plans …
CMS traffic on WAN is 80% SRM, 20% XrootD
  (still, this is much BELOW (10x) the LAN traffic)
Remote access jobs exist and are at least O(10%)

## Slide 20: What are we using today SRM for?
CMS, ATLAS:
  Most of the remote transfers (notable exceptions are XrootD and GridFTP)
  Totality of Tape Interactions
    essential for PrepareToGet/PrepareToPut
LHCb:
  a larger share of Xrootd for remote Disk to Disk transfers
  SRM used as a monitoring tool (space monitoring)
ALICE:
  No SRM at all (Xrootd with site specific stagein/out mechanisms – GEMSS here)

## Slide 21: Medium/Long term statements
Medium Term (up to RunII at least, probably up to RunIII):
  No big changes of utilization pattern
  Steadily increase of streaming accesses, also due to better quality overflow site matching
  Increase in the number of file access / transfer protocols, if they allow for a more widespread access to resources.
  Disk to Disk transfers not really needing SRM, can be ok with GridFTP, Xrootd, Httpd
  SRM remains the tool when tape is involved
  Storm needed at least up to the end of RunIII (2023?)

## Slide 22: Long(er) term
Much more difficult to predict …
One can imagine random access enabled protocols (Xrootd, Httpd, whatever will rise as a standard…) being more widely used also for organized data transfers
Cloud-like storage will start to be much more present, with protocols like S3 and object storage systems a-la Ceph
  Unavoidable if we start buying storage from providers
  But still, this does not exclude the possibility to have SRM as small layer over cloud FSs – StoRM is exactly this
Difficult to state SRM/StoRM will be a total necessity, but still some mean of interaction with tape will be necessary.
  RAL/Ceph is a nice experiment, let’s see if they are really able to satisfy experiments’ needs.

## Slide 23: (non-LHC Experiments) – fast check with the usual suspects
BelleII
  No tape usage until 2020 (@ CNAF)
  Later, they need Buffer->Tape operations and (more critical?) bulk stageout before reprocessing
  Can be served in other ways (like ALICE now), otherwise seems a clear use case for SRM
  Keen to adapt any existing solution, not really willing to implement new ones
Other Exps (mostly Astroparticle) - totalling few PBs all together
  Mostly WriteOnce/ReadNever (custodial copy)
  Write on Buffer, recall on demand (using GEMSS) mostly fine
  For the few cases where bulk recalls are needed, support personnel act by hand
TAPE USAGE (2014-2015) – ALL VOs
TB
“The rest”
If they are asked, they would vote for “anything, but with a Posix interface and a single (virtual) FS”

## Slide 24: Conclusions(?)
At least up to the point we can see now, SRM seems still on the critical path for Experiments
  Mostly (if not only) for tape interactions
  Much less for Disk to Disk transfers
    Used, but there are not negligible exceptions – and, mostly, Experiments would know how to switch even today if needed.
  Some Experiments (LHCb notably) use SRM also as a monitoring/querying tool
    Total space used , …
  Considering RunII as a trivial (!) extension to run II for pp, this would suggest the need for StoRM up to ~2022