## Slide 1
Laser-driven generation of ultra-bright MeV
gamma-rays via non-linear Thomson scattering
HPC @ CNAF
Bologna 24/06/2014
G. Sarri
School of Mathematics and Physics, The Queen‘s University of Belfast, UK

## Slide 2
Main collaborators
M. Zepf, D. J. Corvan
J. Cole, K. Poder,
Z. Najmudin,
S. P. D. Mangles
D. Symes
and ASTRA-GEMINI
technical staff
W. Schumaker, A.G.R. Thomas, K. Krushelnick
A. Di Piazza, C. H. Keitel
M. Yeung

## Slide 3
Talk outline
1. Motivation: - Gamma-rays in medicine and applied physics
2. Experimental techniques: - Undulator vs. Wiggler
- Betatron / Bremsstrahlung / Thomson
        - Towards Compton?
        - Radiation reaction and Compton scattering
3. The experimental results: - Experimental setup
        - Beams synchronisation
        - Gamma-ray detection
        - Ultra-high brightness at high energy
4. Conclusions

## Slide 4
Motivation
HPC @ CNAF
Bologna 24/06/2014

## Slide 5
Motivation: medicine
MeV gamma-ray beams are widely used for cancer radiotherapy
Gamma-rays are used in medicine due to their
effectiveness in killing cells. Bremsstrahlung
radiation is often used, due to the simplicity of
generating it but the poor divergence and source
size gives poor spatial resolution.
Typical values: LINAC’s electron energy range: 4 – 25 MeV
gamma-ray source size: hundreds of microns
gamma-ray divergence: tens of mrad
dose deposited per session: 1 – 2 Gy
X Collimating devices are required for better localisation of the radiation.
They usually induce stray particles in the beam which have detrimental effects on the skin
X Big and expensive machines, with poor knowledge of the effective dose deposited

## Slide 6
Motivation: homeland security
MeV gamma-ray beams are of interest for radiography and active interrogation of materials
Giant Dipole Resonances occur in
a multi-MeV energy range and
induce photofission of the nuclei
with typical by-products signatures
It allows for fast, non-invasive and
safe probing of materials.
Main requirements: compactness, high
repetition rate, high brilliance
(to minimise false positive rates)

## Slide 7
2. Experimental techniques
HPC @ CNAF
Bologna 24/06/2014

## Slide 8
Synchrotron radiation
Electromagnetic waves are emitted by an accelerated charged particle
The electromagnetic power emitted by an accelerated particle is:
If the electron oscillation is linear, the typical energy and flux of gamma-ray energy is:
here a0 and lL are the laser dimensionless intensity
and wavelength, respectively. These hold as long as a0 << 1
If the electron oscillation is non-linear, the typical energy and flux of gamma-ray energy is:
These two regimes are equivalent
to those of a solid-state undulator if:
a0  K
lL/2 lU
Keeping the analogy, a0 << 1 corresponds to an undulator and a0 > 1 to a wiggler

## Slide 9
Betatron
In the laser wake field, the e- undergoes transverse oscillations generating synchrotron radiation
From A. Rousse et al. PRL 2004
Typical electron-laser parameters:
Ee- ~ 0.1 – 1 GeV (g ~ 0.2 – 2 x103)
a0 ~ 1 (K~1)
Typical energies: sub-MeV
Typical divergence: mrad
Brightness: > 1021 phs s-1mm-2mrad-2 0.1% BW
From S. Kneip et al. Nat. Phys. 2009
Despite the good spatial and
temporal qualities, it is not possible to generate photons with multi-MeV energies

## Slide 10
Bremsstrahlung
When propagating through a solid, the electron emits bremsstrahlung radiation
Typical electron parameters:
Ee- ~ 0.1 – 1 GeV (g ~ 0.2 – 2 x103)
Typical energies: tens to hundreds of MeV
Typical divergence: tens of mrad
Typical source size: hundreds of microns
Typical brightness: 1016 phs s-1mm-2mrad-2 0.1% BW
From Y. Glinec et al. PRL 2005
From A. Giulietti et al. PRL 2008

## Slide 11
Thomson scattering
Oscillation of an electron in a laser field generates synchrotron radiation
Typical electron parameters:
Ee- ~ 0.1 – 1 GeV (g ~ 0.2 – 2 x103)
a0 ~ 1 - 20
Typical energies: tens to hundreds of MeV
Typical divergence: mrad
Typical source size: 1 – 20 microns
Brightness: >1019 phs s-1mm-2mrad-2 0.1% BW
Courtesy of D. J. Corvan
Experimental work has demonstrated Thomson scattering only in the linear regime, leading
to gamma-ray energies in the sub-MeV regime.
Extension to the non-linear regime (a0 > 1) would lead to both higher energies and higher
photon yield.

## Slide 12
Laser-driven gamma-ray sources
Non-linear Thomson
scattering allows for high
brightness and high energy
simultaneously, combining
the appealing characteristics
of bremsstrahlung and
betatron radiation
Medicine
GDR

## Slide 13
Compton scattering
In ultra-high intensity, the quantum nature of Thomson scattering becomes non-negligible
Gamma Radiation Reaction
Electron radiation Reaction
Pair production
Electron Straggling
From T. G. Blackburn
et al. PRL 2014

## Slide 14
Conventional accelerators: SLAC
An existing ≈ 100 GeV, 2.4miles long LINAC machine is SLAC
Typical parameters
Energy: ≈ 90 GeV
Polarisation: 80% !
Duration: 10 ps (40 fs if compressed)
Positron density: 5 x 1016 cm-3

## Slide 15
Conventional accelerators: SLAC
Only experimental evidence of non-linear Compton scattering and pair production
From C. Bula et al. PRL 1996
From D. L. Burke et al. PRL 1997

## Slide 16
3. Experimental results
HPC @ CNAF
Bologna 24/06/2014

## Slide 17
Experimental campaign carried out using the GEMINI laser (CLF, RAL)
Experimental setup
1 laser beam for wakefield acceleration:
1 laser beam focussed by a holed F/2
parabola + a spatial random diffuser:
The high-intensity peak of the laser catches a small
portion of electrons (1/100). Only by diffusing the
laser, we achieve a detectable photon yield

## Slide 18
Beam synchronisation
To achieve synchronisation between the two-laser pulses (42±4 fs) we adopted a spectral
interferometric technique:
By measuring the fringe tilt and period
from the intereference of the two
spectrally dispersed beams, temporal
synchronisation of the two pulses was achieved
within ± 50 fs

## Slide 19
Measuring the gamma-ray spectrum
To measure the spectrum of multi-MeV gamma-rays is a non-trivial task. Current detectors
either ensure single-hit or spectrally integrated measurements.
We have thus developed a Compton-based detector. Gamma-rays are converted into
electrons, with similar spectral distribution, which are subsequently spectrally resolved by a
magnetic spectrometer:
~MeV resolution from 1 to 30 MeV

## Slide 20
Measuring the gamma-ray spectrum
High signal-to-noise ratio
High spectral resolution
Compact
Absolutely calibrated
Non-invasive (possibility of
beam profile imaging downstream)
D. J. Corvan et al. RSI (submitted) 2014

## Slide 21
Measured gamma-ray spectra
G. Sarri et al. (submitted) 2014
Gamma-rays with energy per photon reaching 15 – 18 MeV.
Signal drops to zero if artificial temporal delay is introduced and it significantly decreases
if the beams are spatially misaglined.
Measured yield and energy agrees with analytical calculations for a0 = 2 indicating onset
of non-linear Thomson scattering.
Measured divergence of ±2mrad.
Source size of 30 microns
Duration ~30 fs
Calculated brightness of ~2x1019 photons/s/mm2/mrad2 x 0.1% BW

## Slide 22
Laser-driven gamma-ray sources
The brightest source of gamma rays in the energy range of 10-15 MeV, scalable to even higher
energies.
Dose deposited on a
1mm3 biological
sample placed 50cm
away from the source
of the order of 0.15 Gy
Energy range, divergence
and brightness in line
with what requested for
active interrogation of
materials
Compact, inexpensive
and high-repetition
Medicine
GDR

## Slide 23
4. Conclusions
HPC @ CNAF
Bologna 24/06/2014

## Slide 24
Conclusions
First experimental demonstration of non-linear Thomson scattering in a non-perturbative
regime
Spectrally resolved measurements of the generated gamma-ray spectrum indicate an energy
per photon reaching 15 – 18 MeV, with the possibility of scaling it to higher energies.
Experimental data indicate extreme sensitivity to spatial and temporal overlap
Ultra-small divergence (~mrad)
Ultra-small source size (~ 30 microns)
Unprecedented ultra-high brightness in the MeV range
Much better spatial qualities than bremsstrahlung and much higher energy than betatron
Of great interest for practical applications