## Slide 1: fs -time resolved x-ray spectroscopy
Federico Boscherini
Department of Physics and Astronomy
University of Bologna, Italy
federico.boscherini@unibo.it

## Slide 2: X-ray methods in condensed matter studies
X-ray methods are widely used to determine the structure of condensed matter
  Crystals, molecules
  Physics, chemistry, biology
Most common x-ray sources
  «X-ray tubes»
  Synchrotron radiation

## Slide 3: X-ray Emission Spectroscopy
Measurement of the energy of scattered radiation
  inelastic x-ray scattering
Can obtain refined information on electronic structure of particular element in a sample
ID26 @ESRF

## Slide 4: Studies of transient states
Recent great interest in X-ray studies of transient states induced by absorption of visible photons
Extension in X-ray domain of techniques used in the visibile range
Visible pump & x-ray probe
Advantage of X-rays
  Structural sensitivity
  Chemical sensitivity

## Slide 5: Time scales of transient states in condensed matter
Electron excitation: < 1 fs
Charge transfer /electron – electron scattering: 10 fs – 500 fs
Electron – phonon scattering: 100 fs – 10 ps
Processes can be followed in the pump – probe approach with 10 fs x-ray pulses

## Slide 6: Time structure of rings & FELs
Source | Pulse length (fs) | Photons/pulse on sample | Rate (Hz)
Storage ring ESRF multi bunch | 20 × 103 | 102 – 104 | 350 × 106
Storage ring ESRF single bunch | 70 × 103 | 104 – 106 | 360 × 103
ELETTRA multi bunch | 40 × 103 | 102 – 104 | 500 × 106
ELETTRA Single bunch | 70 × 103 | 104 – 106 | 1.2 × 106
Storage ring BESSY slicing | 100 | 10 | 103
FERMI | < 100 | 109 - 1012 | 10 - 50
European X-FEL | 3 – 200 | 109 - 1012 | 10 – 4.5 × 106

## Slide 7: LCLS Free electron laser

## Slide 8: Some interesting recent results

## Slide 9: fs XAS at a Hard X‑ray FEL: Application to Spin Crossover Dynamics
Lemke et al, J. Phys. Chem. 117, 735 (2013)
LCLS, [Fe(bpy)3]Cl2 50 mM solution, Fe K edge
MLCT → High spin occurs with t = 160 fs

## Slide 10: Real-Time Observation of Surface Bond Breaking with an X-ray Laser
M. Dell’Angela et al (Nilsson group), SCIENCE 339, 1302 (2013)
Desorption of CO from Ru(0001)
LCLS, XAS and XES at the O K edge
Evidence for a transient precusor state

## Slide 11: Photo catalysis in TiO2 nanostructures L. Pasquini, L. Amidani, F. Boscherini

## Slide 12: Photo-Electrochemical Cell
Fujishima & Honda, NATURE (1972)
Bak, Nowotny, Rekas, Sorrell, Int. J. Hydrogen Energy (2002)
2H+ + 2e H2
2H2O +4h+2H+ + O2

## Slide 13: Nanoparticle synthesis by IGC in Bologna
He
Mass
Flow
Control
Ti
crucible
substrates
FTM
substrate holder
water
cooling
2°
crucible
LN2
p(He) ≈ 1 mbar
Rotary
pump
Vapor
TiO2 NP,  10 – 20 nm diameter

## Slide 14: TiO2 NPs synthesis by IGC
pristine amorphous
annealed in air 600 °C
A
R
R
R
R

## Slide 15: Time scales
1 fs
 1 -10 ns
10 ns
100 fs
10 fs – 1 ps
scavenger
Dye molecule
100 ps – 10 ns
+ slow interface charge transfers (ms – ms)
Deep trap
Shallow trap

## Slide 16: Transient Ti K edge XAFS at SLS
M. H. Rittmann-Frank et al., Angew. Chem. Int. Ed. (2014)
Edge shift (Ti 4+  Ti 3+ ) occurs after 100 ps.
Due to filling of electron trap localized in Ti (Ti4+ Ti3+)

## Slide 17: High resolution XAS on Au doped TiO2 NP
Au NP increases visible light absorption (surface plasmon resonance)
Differential spectra capture the transient state
In collaboration with Naldoni & Del Santo

## Slide 18: fs XES with LWFA x-rays
The peculiar characteristics of a LWFA Compton x-ray source may allow the realization of fs XES on a laboratory scale
Photon energy range of interest: 5 – 50 keV

## Slide 19: fs XES with LWFA x-rays
Advantages
  10 – 100 fs pulse duration
  No time jitter, stability of pump & probe
  X-ray monochromaticity not important
  No X-ray sample damage
  Repetition rate: 10 Hz OK, consider increase
Critical issues
  Photons/pulse
  Optimized analyzer/detector geometry

## Slide 20: Highly efficient XES instrument
Anklamm et al., RSI 85, 053110 (2014)
HAPG crystal analyzer, CCD detector
100 W m-focus X-ray tube, W anode, polycapillary optics
Ti Kb spectra recorded in 20 min

## Slide 21: Conclusions
fs time resolved XES with LWFA x-rays could provide lab scale probe of transient states in condensed matter with important applications in
  Condensed matter physics
  Chemistry
  Biology
Lower cost alternative to large scale facilites

## Slide 23: X-ray methods
X-rays
Detector
I
angle
X-Ray Diffraction
XRD
Long range
structure

## Slide 24: TiO2
Rutile P42/mnm
Anatase I41/amd
O
Ti
Gap
3.0 eV
Gap
3.2 eV
semiconducting and catalytic properties
long-term photostability and inertness to chemical environments
response to UV-light
  photoelectrode in a photoelectrochemical cell

## Slide 25: A chamber for fs X-ray Experiments at the European XFEL

## Slide 26: FXE beamline at XFEL
Designed for fs XAS, XES/RIXS and diffuse scattering in pump – probe mode
SASE-1 source
XAS: transmission (spectrum analyzer), fluorescence (von Hamos and Johann spectrometers)
XAS/XES/RIXS: von Hamos and Johann spectrometers
Diffuse scattering: Large Pixel Detector

## Slide 27: FXE beamline at XFEL
LPD
Johann
scanning
spectrometer
Sample stage von Hamos spetrometer

## Slide 28: Sample stage and von Hamos spectrometer

## Slide 29: A vacuum chamber compatible with the FXE sample stage